## Slide 1: Aurelien Bouvier
PyVisage: an image analysis package

## Slide 2: Outline
Overview
Installation
Code high-level architecture
Modules description
Tutorials
Useful commands
Upcoming improvements

## Slide 3: Overview 1
Goal: build a modular package for Image processing/analysis intended for efficient sensor characterization
Python advantages:
  Free and open source
  High level
  Simple and elegant object-oriented programming
  Coding is fast thanks to zillions of available modules to help you perform specific tasks
    In particular, powerful matrix/scientific modules available
  Compact programs that are highly readable
PyVisage heavily uses the following python modules:
  numpy
  scipy
  matplotlib

## Slide 4: Overview 2
Software has been written in a modular fashion to simplify maintenance and future development
Current package size: ~2,000 lines
Package is at a reasonable development stage to permit other users to use it and develop further functionalities

## Slide 5: Installation
Minimum packages needed: python2.7, numpy, matplotlib
A python environment that I like a lot is Enthought Canopy which can be downloaded from:
  www.enthought.com/downloads/
  comes pre-installed with all major python modules (numpy, scipy,matplotlib) + Ipython
Mercurial repository:
  \\INVCA-storage\Users\abouvier\PROGRAMS\PyVisage
Run following command in main directory:
  python setup.py install

## Slide 6: Code architecture
ImageArray
Image
Measurement
DarkCurrent
PhotonTransfer
Crosstalk
ReadNoise
PlotTools

## Slide 7: Image.py
Handles single image operations
  Image arithmetic (ex: dark subtraction)
  ROI
  Column swapping
  RTN/FPN corrections
  Channel grouping
  Plotting
    2D image
    histograms
    profiles
ImageArray
Image
Measurement
PlotTools

## Slide 8: ImageArray.py
Handles array of images
  Group operations on all images (calling Image module)
  Image averaging
  Image merging
ImageArray
Image
Measurement
PlotTools

## Slide 9: Measurement.py
Handles analysis of parameter scan
  Batch post-processing
  Calculation of response, noise vs parameter scanned
  Results plotting
High level modules (ReadNoise.py, Crosstalk.py, PhotonTransfert.py) all inherit directly from this module
ImageArray
Image
Measurement
PlotTools

## Slide 10: PlotTools.py
Provides plotting related functions
ImageArray
Image
Measurement
PlotTools

## Slide 11: Image tutorial – dark subtraction
import Image
raw_bright = 'Q8A643w20#44R_Red//Bright_-0.8//image_0.raw'
raw_dark = 'Q8A643w20#44R_Red//Dark_-0.8//image_0.raw'
im_bright = Image.Image(raw_bright)
im_dark = Image.Image(raw_dark)
im_bright.info() # optional
# Dark subtraction
im_bright.subtract(im_dark)
im_bright.plot_image(bsave=True,filename='image_darksubtracted.png')
im_bright.plot_histogram(bsave=True,filename='hist_darksubtracted.png')

## Slide 12: Image tutorial – dark subtraction

## Slide 13: Image tutorial – ROI + channel splitting
import Image
raw_bright = 'Q8A643w20#44R_Red//Bright_-0.8//image_0.raw'
raw_dark = 'Q8A643w20#44R_Red//Dark_-0.8//image_0.raw'
im_bright = Image.Image(raw_bright)
im_dark = Image.Image(raw_dark)
# Dark subtraction
im_bright.subtract(im_dark)
# Channel grouping
im_bright.set_channel_groups((2,2))
# Set ROI in Bayer region
im_bright.set_ROI(2000,2300,1000,1300) # bayer
im_bright.plot_image(bstack=True,bsave=True,filename='image_darksubtracted_roi_channelsplit.png')
im_bright.plot_histogram(bsave=True,filename='hist_darksubtracted_roi_channelsplit.png')
print "horizontal xtalk = %.1f%%"%(Median[1]/Median[0]*100)
print "vertical xtalk = %.1f%%"%(Median[2]/Median[0]*100)

## Slide 14: Image tutorial – ROI + channel splitting

## Slide 15: Image tutorial – RTN correction
import Image
raw_bright = 'Q8A643w20#44R_Red//Bright_-0.8//image_0.raw'
raw_dark = 'Q8A643w20#44R_Red//Dark_-0.8//image_0.raw'
im_bright = Image.Image(raw_bright)
im_dark = Image.Image(raw_dark)
# Dark subtraction
im_bright.subtract(im_dark)
# 2x2 channel grouping
im_bright.set_channel_groups((2,2))
# Set ROI in Bayer region
im_bright.set_ROI(2000,2300,1000,1300) # bayer
# RTN correction
im_bright.RTN_correction() # default columns used: 4-67
im_bright.plot_image(bstack=True,bsave=True,filename='image_darksubtracted_roi_channelsplit_rtncorr.png')
im_bright.plot_histogram(bsave=True,filename='hist_darksubtracted_roi_channelsplit_rtncorr.png')

## Slide 16: Image tutorial – RTN correction
Note: RTN correction is performed on the whole image (not ROI only)
Without RTN correction
With RTN correction

## Slide 17: Useful Image.py methods (1)
info()
set_ROI(rowstart, rowstop, colstart, colstop)
set_center_ROI(roi_dim)
infoROI()
set_channel_groups(channel_groups)
get_array(i_channel_group=None, bstack=False)
get_image_channelsplit()
get_image_channel(i_channel_group)
subtract(image)
divide(image)
multiply(constant)

## Slide 18: Useful Image.py methods (2)
get_median()
get_median_channel_groups():
get_rms(minval=None,maxval=None)
get_rms_channel_groups(bfit=False,nbins=100,Nsigma=3)
column_swap()
FPN_correction(bswap=True, rowstart=0, rowstop=64, target=None)
RTN_correction(bswap=True, colstart=4, colstop=67, target=None, boddeven=False, bsave=False, filename=None)
plot_histogram(channel,xmin, xmax, nbins, blog, figsize, bsave, filename, title, xlabel, ylabel):
plot_image(bstack, minval, maxval, figsize, bsave, filename, title=, bfullresolution)
plot_profile(axis=0, bsave, filename,title=, xlabel, ylabel)

## Slide 19: Useful Image.py methods (3)
save2raw(filename)
save2csv(csvfilename,bverbose)

## Slide 20: ImageArray tutorial
import glob
import ImageArray
file_darks = 'Intro_tutorial\\Q8A636w14#25-D_greenL\\Dark\\DarkImage_*.raw'
raw_images = glob.glob(file_darks)
im_arr = ImageArray.ImageArray(raw_images[:3])
# Average image of all images contained inside im_arr
im_avg = im_arr.average()
#im_avg.plot_image()
import Image
im_ref = Image.Image('Q8A636w14#25-D_greenL\\Dark\\DarkImage_5.raw')
# Perform batch dark subtraction
im_arr.subtract(im_ref)
#im_arr[1].plot_image()
im_arr[1].plot_histogram(xmin=-100,xmax=+100)
print im_arr.Images[1].get_rms()

## Slide 21: ImageArray tutorial

## Slide 22: Useful ImageArray.py methods
set_ROI(rowstart, rowstop, colstart, colstop)
set_center_ROI(roi_dim)
subtract(ref_image)
average()
column_swap()
combine(shape)

## Slide 23: Upcoming improvements
Revision control: Mercurial
Get more people familiar with the software and participating to its development
Expand ImageArray.py capabilities
Consolidate Measurement.py module
Improve comments inside the code for better readability
Build User Interface:
  Menu driven inteface
  GUI driven interface
Data acquisition:
  Interface with qView3
  Build data acquisition module